Smartphone to Fox communication protocol description
by White Fossa aka Artyom Vetrov.
License: AGPLv3+
# Common packet format
Exchange between smartphone and fox is made via Bluetooth-RFCOMM (i.e. via virtual UART).
All packets (both directions) have the same basic structure:
	Full packet length	Payload	CRC
Size	1 byte	1-59 bytes	4 bytes
Description	Full packet length (i.e. including CRC and packet length byte). Value must be [6-64] (fox-side buffer is 64 bytes length).	Just a payload, here can be anything.	Standard CRC32, calculated over full packet length and payload fields.

Packets with wrong full length (i.e. not from [6-64] range) is discarded immediately.
CRC32 is re-calculated on the receiving side after packet reception, packets with incorrect CRC is discarded too.
# Payload type
First byte of payload always specify type of it. Next types are currently supported:
Payload type	Description	First byte value
Command to fox	Command, issued by smartphone. This type of packet is always sent by smartphone and never by the fox.	0x00
Response to command	Response to the command from smartphone. Can be sent only by the fox and only as a response to command.	0x01
Event from fox	Issued by fox when something is happened. Always issued without previous command.	0x02

# Profile-independent commands
This commands affects common, not profile-defined settings of fox (like date and time).
## Set date and time
Issue this command to set fox date and time. Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x00	Set date and time
2	0-99	Year of XXI century
3	1-12	Month (1 is January)
4	1-31	Day of month
5	1-7	Day of week (1 is Monday)
6	0-23	Hour
7	0-59	Minute
8	0-59	Second

Total payload length: 9 bytes.

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x00	Set date and time
2	0x00 or 0payloadx01	Is successful? / 0x00 if successful, / 0x01 if not (for example if time is incorrect).

# Set fox name
Issue this command to set fox name. Note, that setting name also update the bluetooth device name, so it is possible that new pairing will be required.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x01	Set fox name
2	1-32	Name length
3-35	Name bytes	Fox name (without null termination)

payload
Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x01	Set fox name
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (for example if name is too long).

# Get fox name
Issue this command to get fox name.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x02	Get fox name

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x02	Get fox name
2	1-32	Fox name length
3-35	Name bytes	Fox name (without null termination)

# Get profiles count
Issue this command to get count of profiles inside a fox.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x03	Get profiles count

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x03	Get profiles count
2	1-255	Profiles count

# Get profile name
Issue this command to given profile name.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x04	Get profile name
2	0-255	Profile ID

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x04	Get profile name
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (when profile ID is wrong).
3	0-255	Profile ID
4	1-16	Profile name length (have no meaning if not successful)
5-21	Name bytes	Profile name (without null termination)

# Add new profile
Issue this command to add a new profile.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x05	Add profile

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x05	Add profile
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (when there is too much profiles).

# Get current profile ID
Issue this command to get current profile ID

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x06	Get current profile ID

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x06	Get current profile ID
2	0-255	Current profile ID

# Switch to profile
Issue this command to switch to given profile and load fox settings from it. Note, that if fox was armed profile switch disarms her, but only in case if new profile is not current one.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x07	Switch to profile
2	0-255	Profile ID to switch

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x07	Switch to profile
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (when profile ID is incorrect).

# Set profile name
Issue this command to set current profile name.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x08	Set profile name
2	1-16	Profile name length
3-18	Name bytes	Profile name

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x08	Set profile name
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (if name length is incorrect).

# Get frequency
Issue this command to get fox frequency

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x09	Get frequency

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x09	Get frequency
2	0x00 or 0x01	Is 144MHz? / If 0x00 then fox in 3.5MHz range (80m), if 0x01 – then in 144MHz range (2m)
3-6	uint32_t with frequency, least significant byte first	Fox frequency in Hz

# Set frequency
Issue this command to set fox frequency.
Allowed frequency ranges:
- 3500000 – 3650000 Hz for 3.5MHz range
- 144000000 – 146000000 Hz for 144MHz range

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x0A	Set frequency
2	0x00 or 0x01	Is 144MHz? / If 0x00 then fox in 3.5MHz range (80m), if 0x01 – then in 144MHz range (2m)
3-6	uint32_t with frequency, least significant byte first	Fox frequency in Hz

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x0A	Set frequency
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (if frequency outside allowed ranges).

# Get code
Issue this command to get fox code.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x0B	Get fox code

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x0B	Get fox code
2	0-6	0 – Finish (MO) / 1- Fox #1 (MOE) / 2 – Fox #2 (MOI) / 3 – Fox #3 (MOS) / 4 – Fox #4 (MOH) / 5 – Fox #5 (MO5) / 6 – Beacon (S)