Smartphone to Fox communication protocol description
by White Fossa aka Artyom Vetrov.
License: AGPLv3+
# Common packet format
Exchange between smartphone and fox is made via Bluetooth-RFCOMM (i.e. via virtual UART).
All packets (both directions) have the same basic structure:
	Full packet length	Payload	CRC
Size	1 byte	1-59 bytes	4 bytes
Description	Full packet length (i.e. including CRC and packet length byte). Value must be [6-64] (fox-side buffer is 64 bytes length).	Just a payload, here can be anything.	Standard CRC32, calculated over full packet length and payload fields.

Packets with wrong full length (i.e. not from [6-64] range) is discarded immediately.
CRC32 is re-calculated on the receiving side after packet reception, packets with incorrect CRC is discarded too.
# Payload type
First byte of payload always specify type of it. Next types are currently supported:
Payload type	Description	First byte value
Command to fox	Command, issued by smartphone. This type of packet is always sent by smartphone and never by the fox.	0x00
Response to command	Response to the command from smartphone. Can be sent only by the fox and only as a response to command.	0x01
Event from fox	Issued by fox when something is happened. Always issued without previous command.	0x02

# Sleepmodes
All commands with correct CRC reset sleepmodes timer, causing fox to remain active with display turned on. To avoid sleeping it is recommended to use “No operation” command.
# Set date and time
Issue this command to set fox date and time.
This command will fail if fox is armed!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x00	Set date and time
2	0-99	Year of XXI century
3	1-12	Month (1 is January)
4	1-31	Day of month
5	1-7	Day of week (1 is Monday)
6	0-23	Hour
7	0-59	Minute
8	0-59	Second

Total payload length: 9 bytes.

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x00	Set date and time
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (for example if time is incorrect).

# Set fox name
Issue this command to set fox name. Note, that setting name also update the bluetooth device name, so it is possible that new pairing will be required.
This command will fail if fox is armed!

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x01	Set fox name
2	1-32	Name length
3-35	Name bytes	Fox name (without null termination)

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x01	Set fox name
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (for example if name is too long).

# Get fox name
Issue this command to get fox name.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x02	Get fox name

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x02	Get fox name
2	1-32	Fox name length
3-35	Name bytes	Fox name (without null termination)

# Get profiles count
Issue this command to get count of profiles inside a fox.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x03	Get profiles count

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x03	Get profiles count
2	1-255	Profiles count

# Get profile name
Issue this command to given profile name.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x04	Get profile name
2	0-255	Profile ID

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x04	Get profile name
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (when profile ID is wrong).
3	0-255	Profile ID
4	1-16	Profile name length (have no meaning if not successful)
5-21	Name bytes	Profile name (without null termination)

# Add new profile
Issue this command to add a new profile.
This command will fail if fox is armed!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x05	Add profile

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x05	Add profile
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (when there is too much profiles).

# Get current profile ID
Issue this command to get current profile ID

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x06	Get current profile ID

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x06	Get current profile ID
2	0-255	Current profile ID

# Switch to profile
Issue this command to switch to given profile and load fox settings from it.
This command will fail if fox is armed!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x07	Switch to profile
2	0-255	Profile ID to switch

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x07	Switch to profile
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (when profile ID is incorrect).

# Set profile name
Issue this command to set current profile name.
This command will fail if fox is armed!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x08	Set profile name
2	1-16	Profile name length
3-18	Name bytes	Profile name

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x08	Set profile name
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (if name length is incorrect).

# Get frequency
Issue this command to get fox frequency

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x09	Get frequency

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x09	Get frequency
2	0x00 or 0x01	Is 144MHz? / If 0x00 then fox in 3.5MHz range (80m), if 0x01 – then in 144MHz range (2m)
3-6	uint32_t with frequency, least significant byte first	Fox frequency in Hz

# Set frequency
Issue this command to set fox frequency.
Allowed frequency ranges:
- 3500000 – 3650000 Hz for 3.5MHz range
- 144000000 – 146000000 Hz for 144MHz range
This command will fail if fox is armed!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x0A	Set frequency
2	0x00 or 0x01	Is 144MHz? / If 0x00 then fox in 3.5MHz range (80m), if 0x01 – then in 144MHz range (2m)
3-6	uint32_t with frequency, least significant byte first	Fox frequency in Hz

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x0A	Set frequency
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (if frequency outside allowed ranges).

# Get code
Issue this command to get fox code.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x0B	Get fox code

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x0B	Get fox code
2	0-6	Fox code: / 0 – Finish (MO) / 1- Fox #1 (MOE) / 2 – Fox #2 (MOI) / 3 – Fox #3 (MOS) / 4 – Fox #4 (MOH) / 5 – Fox #5 (MO5) / 6 – Beacon (S)

# Set code
Issue this command to set fox code.
This command will fail if fox is armed!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x0C	Set fox code
2	0-6	Fox code: / 0 – Finish (MO) / 1- Fox #1 (MOE) / 2 – Fox #2 (MOI) / 3 – Fox #3 (MOS) / 4 – Fox #4 (MOH) / 5 – Fox #5 (MO5) / 6 – Beacon (S)

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x0C	Set fox code
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (if requested invalid code).

# Get speed
Issue this command to get fox speed.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x0D	Get fox speed

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x0D	Get fox speed
2	0x00 or 0x01	Fox speed: / 0x00 – slow, / 0x01 – fast

# Set speed
Issue this command to set fox speed.
This command will fail if fox is armed!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x0E	Set fox speed
2	0x00 or 0x01	Fox speed: / 0x00 – slow, / 0x01 – fast

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x0E	Set fox speed
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (if requested invalid speed).

# Get cycle
Issue this command to get fox cycle parameters.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x0F	Get fox cycle parameters

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x0F	Get fox cycle parameters
2	0x00 or 0x01	Is continuous transmission? / 0x00 – cyclic transmission, / 0x01 – continuous transmission
3-4	uint16_t, least significant byte first	Transmission time (in seconds), applicable only for cyclic transmission
5-6	uint16_t, least significant byte first	Pause time (in seconds), applicable only for cyclic transmission

# Set cycle
Issue this command to set fox cycle parameters.
This command will fail if fox is armed!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x10	Set fox cycle parameters
2	0x00 or 0x01	Is continuous transmission? / 0x00 – cyclic transmission, / 0x01 – continuous transmission
3-4	uint16_t, least significant byte first	Transmission time (in seconds), applicable only for cyclic transmission, but you must send it in any cases
5-6	uint16_t, least significant byte first	Pause time (in seconds), applicable only for cyclic transmission, but you must send it in any cases

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x10	Set fox cycle parameters
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (too short durations).

# Get ending tone duration
Issue this command to get ending tone duration.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x11	Get ending tone duration

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x11	Get ending tone duration
2	uint8_t	Ending tone duration in seconds

# Set ending tone duration
Issue this command to set ending tone duration.
This command will fail if fox is armed!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x12	Set ending tone duration
2	uin8_t	Ending tone duration in seconds

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x12	Set ending tone duration
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (too long ending tone).

# Get begin and end times
Issue this command to get times when fox will turn on and off.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x13	Get begin and end times

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x13	Get begin and end times
2-5	uint32_t, least significant byte first	Begin time (seconds since midnight)
6-9	uin32_t, least significant byte first	End time (seconds since midnight)

# Is fox armed?
Issue this command to check is fox armed or not. If armed, then it will start to transmit at Begin Time and end at End Time (see “Get begin and end times” command). If fox not armed, it will be in standby forever.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x14	Is fox armed?

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x14	Is fox armed?
2	0x00 or 0x01	0x00 if not armed, / 0x01 if armed

# Arm fox
Issue this command to arm fox. Armed fox will start to transmit at previously set time.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x15	Arm fox

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x15	Arm fox
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (fox already armed, fox example)

Note, that successful answer doesn’t mean that fox is armed, it just signalizing that arming process is started. For arming completion see “Fox armed” event.

# Disarm fox
Issue this command to disarm fox. If fox in countdown before start, then countdown will be aborted and fox will switch to standby mode, if fox already transmitting – transmission will be cancelled.

This command will fail if fox is NOT armed!
This command will fail if antenna matching in progress!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x16	Disarm fox

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x16	Disarm fox
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (internal error during disarming)

# Set begin and end times
Issue this command to set times when fox will turn on and off.
This command will fail if fox is armed!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x17	Set begin and end times
2-5	uint32_t, least significant byte first	Begin time (seconds since midnight)
6-9	uin32_t, least significant byte first	End time (seconds since midnight)

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x17	Set begin and end times
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (End time is earlier or equal to begin time)

# Get output power
Issue this command to get fox output power (float, in watts). Note, that output power is determined only for 3.5MHz mode, for 144MHz fox just returns hardcoded value.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x18	Get fox power

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x18	Get fox power
2-5	float	Fox power in watts

# Set output power
Issue this command to set fox output power (float, in watts). Note, that power is settable only for 3.5MHz mode, if fox in 144MHz mode, then this command will always fail.
This command will fail if fox is armed!
Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x19	Set fox power
2-5	float	Fox power in watts

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x19	Set fox power
2	0x00 or 0x01	Is successful? / 0x00 if successful, / 0x01 if not (incorrect power or 144MHz mode)

# Get battery level
Issue this command to get battery level. Level is represented as a float, where 0 is fully discharged and 1 is fully charged.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x1A	Get battery level

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x1A	Get battery level
2-5	float	Battery level [0-1]

# Get 3.5MHz antenna voltage level (ADC)
This is service command, not intended to regular use. Issue it to get 3.5MHz antenna voltage level in ADC measurements (i.e. not in volts, but raw ADC value, averaged).

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x1B	Get 3.5MHz antenna level (ADC)

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x1B	Get 3.5MHz antenna level (ADC)
2-5	float	Averaged antenna voltage

# Get battery voltage level (ADC)
This is service command, not intended to regular use. Issue it to get battery voltage level in ADC measurements (i.e. not in volts, but raw ADC value, averaged).

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x1C	Get battery level (ADC)

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x1C	Get battery level (ADC)
2-5	float	Averaged battery voltage

# Get 3.5MHz output stage power voltage level (ADC)
This is service command, not intended to regular use. Issue it to get 3.5MHz output stage power voltage level in ADC measurements (i.e. not in volts, but raw ADC value, averaged).

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x1D	Get 3.5MHz output stage power voltage (ADC)

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x1D	Get 3.5MHz output stage power voltage (ADC)
2-5	float	Averaged power source voltage

# Get battery voltage level
This is service command, not intended to regular use. Issue it to get battery voltage level in volts.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x1E	Get battery level (volts)

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x1E	Get battery level (volts)
2-5	float	Averaged battery voltage

# Get 3.5MHz output stage power voltage level
This is service command, not intended to regular use. Issue it to get 3.5MHz output stage power voltage level in volts.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x1F	Get 3.5MHz output stage power voltage (volts)

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x1F	Get 3.5MHz output stage power voltage (volts)
2-5	float	Averaged power source voltage

# Get last failure code
This is service command, not intended to regular use. Issue it to get last failure code from fox.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x20	Get last failure code

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x20	Get last failure code
2-5	uint32_t	Last failure code

# No operation
This command causes no operation. Execute it just to prevent fox from going to sleepmode.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x21	No operation

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x21	No operation

# Get identification data
This command causes fox to identify herself.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x22	Get identification data

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x22	Get identification data
2-5	uint32_t	Signature. Must be 0xF055AF06 if this device is a fox
6-7	uint16_t	Protocol version, must be 0x01
8-9	uint16_t	Hardware revision
10-11	uint16_t	Software version (for given hardware). It is possible that two versions can exist with the same number for different hardware revisions.
12-15	uint32_t	Fox serial number.

# Get antenna matching status
This command causes fox to provide antenna matching status.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x23	Get antenna matching status

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x23	Get antenna matching status
2	uint8_t	Status: / 0 – matching never was initiated / 1 – matching in progress / 2 – matching completed
3	uint8_t	New for app: / 0x00 if app saw this matching / 0x01 if not
4	uint8_t	Total matcher positions
5	uint8_t	Current matcher position (starting from 0)
6-9	float	Current antenna voltage
10	uint8_t	Current best match position
11-14	float	Current best match voltage (in volts)

# Get antenna matching data
This command causes fox to return data about one matcher position.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x24	Get antenna matching data
2	uint8_t	Requested position

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x24	Get antenna matching data
2	uint8_t	0x00 if successful / 0x01 if requested position is incorrect
3-6	float	Requested position antenna voltage (in volts)

# Mark matching data as seen
This command marks matching data as seen by app

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x25	Mark matching as seen

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x25	Mark matching as seen

# Check for profile settings changes
This command checks if there are any profile settings changes since last call of this command. Only changes, made via fox controls will be reported. Profile switch itself doesn’t count as change.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x26	Check for profile settings changes

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x26	Check for profile settings changes
2	uint8_t	0x00 – no changes / 0x01 – there were some changes

# Reset last failure code
This command resets last failure code to 0 (i.e. to OK).

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x27	Reset last failure code

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x27	Reset last failure code

# Update serial number
Use this command to update fox serial number (for example after EEPROM damage).

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x28	Update serial number
2-5	uint32_t	New serial number

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x28	Update serial number

# Get Ubatt(ADC) to Ubatt(Volts) factors
Use this command to get factors, used to convert ADC value to battery voltage. Ubatt(Volts) = A * Ubatt(ADC) + B

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x29	Get Ubatt(ADC) to Ubatt(Volts) factors

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x29	Get Ubatt(ADC) to Ubatt(Volts) factors
2-5	float	Factor A
6-9	float	Factor B

# Set Ubatt(ADC) to Ubatt(Volts) factors
Use this command to set factors, used to convert ADC value to battery voltage. Ubatt(Volts) = A * Ubatt(ADC) + B. Note, that there is no values control at the fox side.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x2A	Set Ubatt(ADC) to Ubatt(Volts) factors
2	uint8_t	Reset: / 0x00 – do not reset factors to factory defaults; / 0x01 – reset factors to factory defaults. / In case of reset Factor A and Factor B are ignored.
3-6	float	Factor A
7-10	float	Factor B

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x2A	Set Ubatt(ADC) to Ubatt(Volts) factors
2	uint8_t	0x00 if successful, / 0x01 if not. / For now it always successful.

# Get Ubatt(Volts) to battery level factors
Use this command to get factors, used to convert battery voltage to battery level. Level = A * Ubatt(Volts) + B

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x2B	Get Ubatt(Volts) to level factors

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x2B	Get Ubatt(Volts) to level factors
2-5	float	Factor A
6-9	float	Factor B

# Set Ubatt(Volts) to battery level factors
Use this command to set factors, used to convert battery voltage to battery level. Level = A * Ubatt(Volts) + B. Note, that there is no values control at the fox side.

Payload format:
Payload byte	Value	Description
0	0x00	Command to fox
1	0x2C	Set Ubatt(Volts) to level factors
2	uint8_t	Reset: / 0x00 – do not reset factors to factory defaults; / 0x01 – reset factors to factory defaults. / In case of reset Factor A and Factor B are ignored.
3-6	float	Factor A
7-10	float	Factor B

Fox will answer:
Payload byte	Value	Description
0	0x01	Response to command
1	0x2C	Set Ubatt(Volts) to level factors
2	uint8_t	0x00 if successful, / 0x01 if not. / For now it always successful.

# Entering sleepmode event
This is an event, signalizing that fox is going to sleepmode immediately after it. Control software have to drop connection after it.

Payload byte	Value	Description
0	0x02	Event
1	0x01	Entering sleepmode